## Slide 1: CSMA/CD and Ethernet
CSMA with Collision Detection (CD) capability
– Nodes able to detect collisions
– Upon detection of a collision nodes stop transmission Reduce the amount of time wasted on collisions
• Protocol:
– All nodes listen to transmissions on the channel
– When a node has a packet to send: Channel idle => Transmit Channel busy => wait a random delay (binary exponential backoff)
– If a transmitting node detects a collision it stops transmission
Waits a random delay and tries again

## Slide 2: Token Ring
Token rings were developed by IBM in early 1980’s
• Token: a bit sequence
– Token circulates around the ring
Busy token: 01111111
Free token: 01111110
• When a node wants to transmit
– Wait for free token
– Remove token from ring (replace with busy token)
– Transmit message
– When done transmitting, replace free token on ring
– Nodes must buffer 1 bit of data so that a free token can be changed to a busy token
• Token ring is basically a polling system Token does the polling

## Slide 3: Release of Token
Release after transmission
– Node replaces token on ring as soon as it is done transmitting thepacket
– Next node can use token after short propagation delay
• Release after reception
– Node releases token only after its own packet has returned to it Serves as a simple acknowledgement mechanism

## Slide 4: Token ring Issues
Fairness: Can a node hold the token for a long time
– Solution: maximum token hold time
• Token failures: Tokens can be created or destroyed by noise
– Distributed solution:
Nodes are allowed to recognize the loss of a token and create a new token
Collision occurs when two or more nodes create a new token at the same time => need collision resolution algorithms
• Node failures: Since each node must relay all incoming data, the failure of a single node will disrupt the operation of the ring
• Token ring standard: IEEE 802.5

## Slide 5: FDDI
• Fiber distributed data interface (FDDI) is a 100 Mbps Fiber OpticToken Ring local area network standard
• FDDI uses two counter-rotating rings
– Single faults can be isolated by switching from one ring to the other on each side of fault.
• Token release after transmission
• Limit on token hold time
• Upper-bound on time betweentoken visits at a node
– Support for guaranteed delays
– Imposes a limit on the size of a ring
• FDDI designed to be a metro or campus area network technology

## Slide 6: Token BUSES
Special control packet serves as a token
• Nodes must have token to transmit
• Token is passed from node to node in some order
– Conceptually, a token bus is the same as a token ring
– When one node finishes transmission, it sends an idle token to the next node (by addressing the control packet properly)
– Similar to a polling system
• Issues
– Efficiency lower than token rings due to longer transmission delay for the packets and longer propagation delays
– Need protocol for joining and leaving the bus

## Slide 7: Migration to switched LAN
Traditional Ethernet
– Nodes connected with coax Long “runs” of wire everywhere
– CSMA/CD protocol
• “Hub” Ethernet
– Nodes connected to hub Hub acts as a broadcast repeater Shorted cable “runs”, Useful for 100 Mbps
– CSMA/CD protocol
– Easy to add/remove users
– Easy to localize faults
– Cheap cabling (twisted pair, 10baseT)
• Switched Ethernet
– No CSMA/CD
- Easy to increase data rate (e.g., Gbit Ethernet)
– Nodes transmit when they want
– Switch queues the packets and transmits to To otherdestination Switchs
– Typical switch capacity of 20-40 ports
– Each node can now transmit at the full rate of 10/100/Gbps
– Modularity: Switches can be co